## Slide 1
CAE Support
January 2021
CAE Orientation for Consultants – Bentley V8i
CAE Support

## Slide 2: Overview
This presentation provides an overview of the Washington State Dept. of Transportation (WSDOT) Computer Aided Engineering (CAE) environment.
It is intended for consultants who are tasked with developing and delivering WSDOT project data using MicroStation and InRoads V8i.

## Slide 3: Overview - What’s Covered
Introduction to WSDOT Computer Aided Engineering (CAE)
Supported Applications
Standards Manuals
Supporting Resources
Project Organization
File Naming Conventions
Element Conventions
Process Overviews
ProjectWise
WSDOT CAE Environment setup
Quick Tour
Getting Help

## Slide 4: Intro to WSDOT CAE
The Computer Aided Engineering environment at WSDOT covers the following areas of work:
  Field survey data processing
  Design roadway geometrics analysis and engineering
  Computer Aided Drafting (CAD) functions
  Construction administration support
  As-built deliverables
  Engineering drawing\document management

## Slide 5: Supported Applications
WSDOT currently accepts deliverables in the following formats:
  Deliverable File Formats Bentley MicroStation V8i SS3 (v8.11.09.xx) and PowerInRoads V8i SS2 (v8.11.07.xx), are the official WSDOT drafting and design applications and versions. All deliverables to WSDOT shall be in the official version and produced using current CAE resources unless otherwise stated in a specific WSDOT-Consultant agreement. WSDOT is developing an environment for the Bentley Connect and platform anticipates piloting it (internal only) 2021. WSDOT IS NOT accepting any Connect platform deliverables at this time.
This information is published on our public web site:
  www.wsdot.wa.gov/Design/CAE

## Slide 6: Standards Manuals
WSDOT standards manuals applicable to CAE processes include (but are not limited to):
  WSDOT Design Manual
    (www.wsdot.wa.gov/Publications/Manuals/M22-01.htm)
  WSDOT Plans Preparation Manual
    (www.wsdot.wa.gov/Publications/Manuals/M22-31.htm)
  WSDOT Electronic Engineering Data Standards Manual
    (www.wsdot.wa.gov/Publications/Manuals/M3028.htm)
  WSDOT Highway Surveying Manual
    (www.wsdot.wa.gov/Publications/Manuals/M22-97.htm)
  WSDOT Construction Manual
    (www.wsdot.wa.gov/Publications/Manuals/M41-01.htm)

## Slide 7: Supporting Resources
WSDOT CAE has developed a custom resource environment for CAE applications, including MicroStation, InRoads, and survey tools. This environment supports Agency deliverable requirements, and production dataflows to achieve them.
For V8i, this environment is powered by a central resource database that contains settings, attributes and parameters for all CAE applications. This ensures that the resources are synchronized and cross-referenced between applications. That database both generates foundational resource files, but also supports associated custom productivity tools.
Working units are US Survey Foot and Inches. Use provided seed files!
  Project footprint data files (Base files) are in US Survey Foot. = PSE_Base.dgn
  Sheet files may be in the following as determined by the WSDOT Project Office:
    US Survey Foot for single-sheet per file and geographically correct sheets = PSE_Base.dgn
    Inches for single- or multiple-sheet per file approaches = PSE_Sheet.dgn

## Slide 8: Supporting Resources MicroStation
The CAE environment includes a comprehensive CAD element list in support of all WSDOT project deliverables development.
MicroStation is the foundation of the platform
  WSDOT uses a user-friendly alpha based element and level naming convention.
  The central database contains approximately 2400 CAD elements and assigns the appropriate attributes, cell (if applicable), and text characteristics to each.
  All standard deliverable levels, lines styles, fonts, and cells are provided along with supporting base functional resources for printing and other processes.
  WSDOT utilizes ByLevel attributes for all levels and for the most part, a 1-to-1 level to element approach.
  Supporting DGN seed files are provided.

## Slide 9: Supporting Resources InRoads
For InRoads
  A comprehensive set of Feature-, Geometry-, Named-, and Survey- Symbology are included in the CAE environment via a centralized XIN template file.
  Additional resources support WSDOT standards to each process in the InRoads workflow.
  Agency standard survey field codes are processed into CAE element features via the XIN.
  The environment also includes:
    an InRoads Template Library (ITL) of typical components
    Standards files for Stopping Sight Distance, Superelevations, and other process criteria per the WSDOT Design Manual.
    Preferences to support various scaled plotting of Cross Sections.
    A comprehensive report style sheet library.
    And much more.

## Slide 10: Project Organization
WSDOT projects are standardized and include:
  A consistent folder structure
  Repository for project-specific resources
    Cells and other resource files unique to the project that are generated by the project staff in complement to the Agency standards.
  Discipline-specific workspaces
  The deliverable requirements for each discipline
  Defined in the WSDOT Electronic Engineering Data Standards (EEDS) Manual, Deliverables 3 Project Directory Structure and Deliverables 8 ProjectWise.
    www.wsdot.wa.gov/Publications/Manuals/M3028.htm

## Slide 11: File Naming Conventions
Standardized file naming conventions provide uniformity in structure and greater ease when searching for data, and stable performance.
  Keep file names to minimum practical length
  Do not use special characters in folder or file names
WSDOT applies standard naming conventions for each discipline. For example:
  CAD\Plans Production (MicroStation) files
    [PlanSheetNumber]_Work Order_FileType_PlanType_PlanRefNumber
    00025_XL1234_PS_AL_003.DGN
      This is sheet AL3 which is sheet 25 in the overall contract plan set.
See the EEDS Manual, Deliverables 4 File Naming Conventions.
  www.wsdot.wa.gov/Publications/Manuals/M3028.htm
See WSDOT CAE Tech Notes (www.wsdot.wa.gov/design/cae/technotes.htm)
  CAE Standards Quick Reference Guide (wa.gov)
See Microsoft guidance on path and file naming convention limitations in Windows
  https://docs.microsoft.com/en-us/windows/win32/fileio/naming-a-file

## Slide 12: Element Naming Conventions
WSDOT uses an environment-wide standard element naming convention for drafting and engineering elements.
Survey uses short codes for efficient field data collection that get translated to the engineering convention via InRoads survey data processing.
  See Field Code Report - By Code (wa.gov)
WSDOT uses a Major (Parent) _ Minor (Child) _ Element approach
  Parent Category = Drainage (DR)
  Child Category = Structures (ST)
  Element = CatchBasin
See WSDOT CAE Standards Quick Reference Guide (wa.gov)
DR_ST_CatchBasin

## Slide 13: Process Overview
Quantities Extraction
Survey [InRoads for processing]
Design [InRoads]
Drafting [MicroStation]
Construction [InRoads & MicroStation]
Archive Final Project Data
Surface *.DTM
Geometry *.ALG
Roadway Modeler
Quantities Extraction
Baseplan Development
PS&E Plan Generation
Field Survey
Cadastral & Right-of-Way Data
Construction Administration
As-Built Documentation

## Slide 14: Process Overview
Field Survey
InRoads Design
MicroStation Drafting
survey_wsdot.fwf
Field Code
Named Symbology
Geometry Style
Feature Style
Cell Name
Linestyle
Color
Weight
Level Name
wsdot_standards.xin
WSDOT.DGNLib
WAE*.cel
LStyles.rsc
wsdot_standards.xin

## Slide 15: ProjectWise
ProjectWise is a project collaboration and architecture, engineering, construction, (AEC) information management software.
It allows full collaboration between workgroups made up of staff both internal and external to WSDOT.
ProjectWise uses a folder\document structure similar to Windows Explorer.
Contact WSDOT CAE Support for access and support.

## Slide 16: WSDOT CAE Environment Setup
Step 1 – Download the WSDOT V8i resource WinZIP
  Computer Aided Engineering - Resource Updates | WSDOT (wa.gov)
  WSDOT CAE installation instructions (wa.gov)
Step 2 – Extract the resource set to a central location
Step 3 – Create a shortcut with the appropriate switch content.
  “Application EXE” –wsWSDOT_Resources=[central location/]
Add WSDOT.cfg file to workstation Application Install structure
Test shortcut.
You should see

## Slide 17: Quick Tour
WSDOT custom tools are accessed from the WSDOT pull down.
  Place WSDOT Items
  Driven by our central database
  Set drawing Scale
  Browse through standard categories and lists
  Pick an element
  Double-click to place
  Search for elements

## Slide 18: Quick Tour
WSDOT custom tools are accessed from the WSDOT pull down.
  Custom Tools
  Browse through categories of custom tools
  Double-click to activate
  Click once to enable the View Help File button for instructions.

## Slide 19: Quick Tour
WSDOT custom tools are accessed from the WSDOT pull down.
  Print Sheets
  Exclusive to PSE_Sheet seed based files
  Specific to historic WSDOT custom 40 sheet border per file approach.
  Relies on Place\ Label sheet utility in Custom Tools > Sheet Utilities
  Contact your WSDOT Project Office for sheet method require- ments.

## Slide 20: Quick Tour
CAEHelp provides resources to get more info down.
Ask WSDOT CAE Support – sends quick question to WSDOT HQ CAE Help Desk
Contacts – quick link to our contacts website
Tech Notes – links to our library of tech notes and process instructions
Home Page – links to our main external home page

## Slide 21: Getting Help
Computer Aided Engineering - Support | WSDOT (wa.gov)
  (www.wsdot.wa.gov/Design/CAE)
WSDOT Statewide CAE Help Desk hqcaehelpdesk@wsdot.wa.gov
  Keith Anderson – Help Desk Supervisor
  Aaron Cleveland – ProjectWise Admin
  Mike Garcia – CAE Support Engineer
  Jeff Graham – Survey Support
  Clint Hill – CAE Support Manager
Regional CAE Support Staff
  James An – Northwest Region
  Andy Hash – Northwest Region
  Phil Walker – Southwest Region
  Mark Morin– State Ferries
Emailing the CAE Help Desk is the best option as all staff are teleworking